## Slide 1: DESIGN AND IMPLEMENTATION OF VOLTAGE STABLIZER USING DC MOTOR
PROJECT GROUP-ll
GROUP MEMBERS:
AKSHAY MOHANDAS
ANUPAMA REJY
ERWIN THOMAS
MILAN SYAM
SHEENA SEBASTIAN
MAIN GUIDE:
MR.JAISON JAMES
HOD OF EEE DEPARTMENT
CO-GUIDES:
MS.ANJU P
ASST. PROF. EEE
MS.SHRUTHI S NAIR
ASST.PROF.EEE
MR. DEEPU VS
ASST.PROF.EEE

## Slide 2: CONTENTS
INTRODUCTION
OBJECTIVE
HARDWARE SETUP
METHODOLOGY
ALGORITHM
RESULTS
CONCLUSION

## Slide 3: INTRODUCTION
Why Voltage Stabilization is Important?
Electrical systems often experience voltage fluctuations due to factors like power grid issues, weather, or heavy load conditions.
What does a Voltage Stabilizer do?
The voltage stabilizer is designed to maintain a stable output voltage by adjusting to the fluctuating input voltage levels.
Here in the setup we use a DC motor to control an autotransformer.

## Slide 4: OBJECTIVE
“To design, develop, and evaluate a voltage stabilizer that effectively regulates output voltage by dynamically compensating for fluctuations in input voltage”.
This ensures the safe and reliable operation of electrical equipment. The stabilizer works by dynamically adjusting the output voltage with the help of a DC motor and an autotransformer.

## Slide 5
INPUT AND OUTPUT VOLTAGE SENSOR
MOTOR DRIVER
MOTOR
AUTOTRANSFORMER
OUTPUT VOLTAGE
INPUT AC VOLTAGE
MICROCONTROLLER
HARDWARE SETUP
BLOCK DIAGRAM

## Slide 6: COMPONENTS
AUTO TRANSFORMER
ZMPT101B (VOLTAGE SENSOR,250v)
ARDUINO UNO
POTENTIOMETER (10K)
ROTARY ENCODER (EC11)
MOTOR DRIVER(BTS7960, 6-27V,43A)
DC MOTOR(12V,10A)
SMPS(SWITCHED MODE POWER SUPPLY)
BUCK CONVERTER(LM2596)
16 X 4 LCD DISPLAY
Auto Transformer
Buck Converter
SMPS
ZMPT101B
Rotary Encoder
16 x 4 LCD Display
Motor Driver(BTS7960)
Motor
Gear

## Slide 7
CIRCUIT DIAGRAM
Input voltage
Output voltage
motor driver
DC motor
Encoder
Potentiometer

## Slide 8: GEAR DESIGN AND CALCULATION
Gear used ‘SPUR GEAR’, it is a cylindrical gear with straight teeth that are parallel to its axis of rotation.
Module
Pitch Circle Diameter, Face Width
Number of Teeth
Pressure Angle, Clearance
Addendum, Dedendum
Gear Ratio, Material Selection

## Slide 9
Module (M) : The ratio of the pitch diameter to the number of teeth. D/T
Pitch Circle Diameter (PCD) : The diameter of the imaginary circle that represents the gear's effective size. M*T
Number of Teeth (T) : The total count of teeth on the gear.
Pressure Angle: The angle between the gear tooth profile and the line tangent.
Addendum :The distance between the pitch circle and the top of the tooth.
Dedendum : The distance between the pitch circle and the bottom of the tooth.
Clearance : The gap between the top of a tooth on one gear and the bottom of the mating gear's tooth
Face Width: The width of the gear tooth measured parallel to the axis
GEAR DESIGN CONTI….

## Slide 10
Gear Ratio :The ratio of the number of teeth between the driving gear and the driven gear.(T2/T1)
Material Selection : Gear material (e.g., steel, brass, plastic) is crucial based on load, speed, and durability requirements.
GEAR DESIGN CONTI….

## Slide 11: CALCULATION
I/p speed =40 rpm
o/p speed =10 rpm
Gear ratio = 48/12=4 ; (1:4 reduction)
Gear teeth count = T2driven/T1driver
T1 = 12 teeth and T2 = GR*T1 = 48teeth
PCD (for T1) = M*T=2*12 = 24mm; (for T2) = 2*48 = 96mm
Module (D/T)=24/12 = 2mm (for T1) and 96/42=2mm(for T2)
Pressure Angle = 20 degrees (common)
Addendum (1*M) = 2 ; Dedendum = (1.25*M) = 2.5
(T1-driver gear
T2-driven gear)

## Slide 12: GEAR SPECIFICATION
Module: 2mm
No .of teeth: 12
Pressure angle: 20°
Face width: 30mm
Clearance: 0.2mm
Pitch Diameter: 24mm
Addendum : 2mm
Dedendum : 2.5mm
Material: plastic, PLA
Bore diameter/hole for shaft: 8.3mm
Driver Gear (T1)
Module: 2mm
No .of teeth: 48
Pressure angle: 20°
Face width: 10mm
Clearance: 0.2mm
Pitch Diameter: 96mm
Addendum: 2mm
Dedendum: 2.5mm
Material: Plastic, PLA
Bore diameter/hole for shaft: 10mm
Driven Gear (T2)

## Slide 13: CALIBRATION OF VOLTAGE SENSOR
ZMPT101B module is connected to the Arduino (Vcc, GND, Signal OutputA0) and AC supply is given to its other end.
Use Arduino code to read the analog signal from the ZMPT101B and convert it to voltage.
Use a multimeter to measure the real AC voltage from your source.
On the module, there’s a (potentiometer). Slowly turn it while comparing Arduino reading with the multimeter reading.

## Slide 14: CALIBRATION OF POTENTIOMETER
Potentiometer is connected to the Arduino (Vcc, GND, Output-A1)
Use Arduino code to read the analog reading from the potentiometer and convert it to voltage.
Multiply the multiplication factor (46) with raw reading (230/5 ).

## Slide 15: METHODOLOGY
Input Voltage Sensing
Control Mechanism
DC Motor Adjustment
Output Voltage Regulation

## Slide 16: ALGORITHM
Setup phase
Main loop execution
Update encoder
Update voltage
Control motor
Update display

## Slide 17: SIMULATION
Fig:1 simulation
Fig:2 simulation

## Slide 18: RESULTS
Table:1 Observation from hardware setup
ARC LENGTH=2*Pi*r(theta/360)

## Slide 19: Table:2 Readings from stabilizer
INPUT VOLTAGE | OBTAINED OUTPUT VOLTAGE | DESIRED VOLTAGE | ANGLE OF ROTATION
230 | 113 | 110 | 90
220 | 111 | 110 | 114
200 | 110 | 110 | 157
150 | 107 | 110 | 207
100 | 106 | 110 | 319
(With ± 5%tolerance)
OBSERVATION CONTI….

## Slide 20
Chart: Input Supply Voltage
| 230 | 220 | 200 | 150 | 100
Output Voltage | 110 | 110 | 110 | 107 | 106
Desired Voltage | 110 | 110 | 110 | 110 | 110
Angle | 90 | 114 | 157 | 207 | 319
OUTPUT VOLTAGE ,DESIRED VOLTAGE ,ANGLE
Plottings of significant voltages (Inclusive of respective angles)

## Slide 21
PRODUCT
Fig:1 Side view
Fig:2 Top view(without assembling)

## Slide 22: CONCLUSION
The voltage stabilizer effectively regulates output voltage by dynamically compensating for input voltage fluctuations.
It ensures the safe and reliable operation of electrical equipment, protecting them from potential damage.
The system employs a DC motor and an autotransformer to dynamically adjust the output voltage.

## Slide 23: THANK YOU

## Slide 24: PROGRAM

## Slide 25
PROGRAM
Conti….

## Slide 26
PROGRAM
Conti….

## Slide 27
PROGRAM
Conti…..

## Slide 28
PROGRAM
Conti….

## Slide 29
PROGRAM
Conti….

## Slide 30
PROGRAM